## Slide 1
Dr2xml session
Gaëlle Rigoudy, CNRM, Meteo-France
Marie-Pierre Moine, Cerfacs
and the XIOS Team !
XIOS-dr2xml Training, 15-19 March 2021 0

## Slide 2: Outline
Introduction
  Dr2xml, what’s this?
  Brief history
  The CMIP6 Data Request
General features
  Utility
  Cautions
  Simple functional scheme
  The ping file
Usage
  Installation
  Configuration
  Execution
  Verification
Functionalities
  Basic functions
  Customisation
  Extended usage
Dr2xml
GR XIOS-dr2xml Training, 15-19 March 2021 1

## Slide 3: a) dr2xml, what’s this?
1. Introduction
Python tool
XIOS file-def XML writer
  fields and attributes (« variable » in XIOS vocab) in file
  Automatic implementation of XIOS spatial & temporal filters
  Automatic NetCDF file handling (naming, time-splitting, metadata, append write…)
Useful for :
  XIOS-enabled models (output management)
  large number of fields to output
  standard data (format and content)
  adding a lot of mandatory attributes in the
  netCDF output files
GR XIOS-dr2xml Training, 15-19 March 2021 2
CMIP6 production
  Systematic production of CMIP6 compliant CF-netCDF files
  Satisfying the CMIP6 Data Request
CMIP6 data request

## Slide 4
Born with CMIP6 (Data Request)
Development started in sept. 2016 (S. Sénési, CNRM + M.P Moine, Cerfacs)
Now developed & maintained by G. Rigoudy, CNRM
Developed in close collaboration with the XIOS-dev Team (a lot of functionalities introduced in XIOS for CMIP6/dr2xml needs)
Used at IPSL and CNRM-CERFACS in climate models doing CMIP6
  At CNRM-CERFACS: embedded in the modelling workflow (ECLIS)
  At IPSL : used upstream of the modelling workflow (LibIGCM)
All along the dev period, phasing with:
  The CMIP6 Data Request versions
  The CMIP6 Controlled vocabulary
Stabilized version in July 2018 for CMIP6 (v1.13)
Last evolutions:
  Code modularization
  New functionalities
  Python 3 - PEP8
Sources on Github: https://github.com/rigoudyg/dr2xml
ReadtheDocs documentation : https://dr2xml.readthedocs.io/en/documentation/ (not yet finalized)
b) brief history
1. Introduction
GR XIOS-dr2xml Training, 15-19 March 2021 3

## Slide 5
c) the CMIP6 Data Request
1. Introduction
MP XIOS-dr2xml Training, 15-19 March 2021 4
Concretely :
  Is a data base with:
    a python API (facilitates automated interrogation of the data base)
    a browsable html interface
  That gives, for each CMIP6 simulation:
    the variables that should be output (according to the selected priority)
    on which grid/domain/levels
    over which time period
    at which frequency
    with which netCDF attributes...
  CMIP6 DR python API is used by dr2xml
http://clipc-services.ceda.ac.uk/dreq/index.html
Big picture :
  Developed for CMIP6 by Martin Juckes since 2016 to…
  Meet the challenge of model/MIP objectives/experiment design complexity and exposing number/diversity of diagnosis requested by each MIP
  Fully enable the intercomparison :
  « The thousands of diagnostics generated at each centre from hundreds of simulations should be produced and documented in a consistent manner to facilitate meaningful comparisons across models. Hence, for each experiment the MIPs have requested specific output to be archived and shared via the Earth System Grid Federation (ESGF), and the CMIP6 organisers have imposed requirements on file format and metadata »

## Slide 6: a) dr2xml utility
Management of complex and various outputs, supporting:
  all physical field shapes (1D, 2D, 3D, 4D, time-varying or constant)
  all output frequencies (yearly, monthly, daily, 6-hourly, 3-hourly, 1-hourly, sub-hour)
  choice of sampling period
  on the fly diagnostic computation (ex. zonal means, interpolation on pressure levels, on observation sites…)
  allows multivariate diagnostics (computing a diagnostics depending on 2 or more model native variables)
Avoids time-consuming post-processing steps:
  no need to use CMOR
  nor any other offline post-processing steps (even for diagnostic computation)
  formatting/standardisation directly ensured (file names, global and local attributes, temporal axis)
Reduced risk of errors
  “all included” and integrated post-processing
  one tool does all : XIOS !
  homogeneity, coherence, reliability, robustness
2. General features
MP XIOS-dr2xml Training, 15-19 March 2021 5

## Slide 7: b) cautions
One shot ! which means…
  no safety net once the production started
  all requested output and output you need must be there !
Before running the whole simulation:
  Dr2xml configuration must be carefully checked (a verbose log file enables to visualize the planned output variables)
  It is highly recommended to perform a short test run and control/validate the output netCDF files, for e.g. with NCTIME and potentially PrePARE (if the simulation is a CMIP6 one)
2. General features
MP XIOS-dr2xml Training, 15-19 March 2021 6

## Slide 8: c) simple functional scheme
2. General features
MP XIOS-dr2xml Training, 15-19 March 2021 7
DR2XML

## Slide 9: c) simple functional scheme
2. General features
User’s
experiment choices
User’s information about model/lab
configures
MP XIOS-dr2xml Training, 15-19 March 2021 8
DR2XML

## Slide 10: c) simple functional scheme
2. General features
User’s
experiment choices
User’s information about model/lab
MIPs
experiments
institutions
models, …
Thesaurus:
uses
configures
MP XIOS-dr2xml Training, 15-19 March 2021 9
Data Reference Syntax (DRS)
CMIP6 Controlled Vocabulary (CV)
File naming + tree directory conventions
DR2XML

## Slide 11: c) simple functional scheme
2. General features
User’s
experiment choices
User’s information about model/lab
CMIP6 Data Request (DR)
MIPs
experiments
institutions
models, …
Thesaurus:
uses
configures
queries
MP XIOS-dr2xml Training, 15-19 March 2021 10
Data Reference Syntax (DRS)
CMIP6 Controlled Vocabulary (CV)
File naming + tree directory conventions
Requested output variables according to the experiment [priority level, member, period], chosen
DR2XML

## Slide 12: c) simple functional scheme
2. General features
User’s
experiment choices
User’s information about model/lab
CMIP6 Data Request (DR)
MIPs
experiments
institutions
models, …
Thesaurus:
CMOR name
shape
frequency
compute method (ex. temporal mean, spatial mean, masking)
metadata (ex. long name, standard name, units, description)
For each variable, get:
« List » of variables to output
uses
configures
queries
builds
MP XIOS-dr2xml Training, 15-19 March 2021 11
Data Reference Syntax (DRS)
CMIP6 Controlled Vocabulary (CV)
File naming + tree directory conventions
Requested output variables according to the experiment [priority level, member, period], chosen
DR2XML

## Slide 13: c) simple functional scheme
2. General features
User’s
experiment choices
User’s information about model/lab
CMIP6 Data Request (DR)
MIPs
experiments
institutions
models, …
Thesaurus:
CMOR name
shape
frequency
compute method (ex. temporal mean, spatial mean, masking)
metadata (ex. long name, standard name, units, description)
For each variable, get:
« List » of variables to output
uses
configures
builds
implements
XIOS spatial and temporal filters
MP XIOS-dr2xml Training, 15-19 March 2021 12
Data Reference Syntax (DRS)
CMIP6 Controlled Vocabulary (CV)
File naming + tree directory conventions
Requested output variables according to the experiment [priority level, member, period], chosen
DR2XML
queries

## Slide 14: c) simple functional scheme
2. General features
User’s
experiment choices
User’s information about model/lab
CMIP6 Data Request (DR)
MIPs
experiments
institutions
models, …
Thesaurus:
CMOR name
shape
frequency
compute method (ex. temporal mean, spatial mean, masking)
metadata (ex. long name, standard name, units, description)
For each variable, get:
« List » of variables to output
uses
configures
queries
builds
implements
XIOS spatial and temporal filters
MP XIOS-dr2xml Training, 15-19 March 2021 13
glues
CMOR standard attributes
Data Reference Syntax (DRS)
CMIP6 Controlled Vocabulary (CV)
File naming + tree directory conventions
Requested output variables according to the experiment [priority level, member, period], chosen
DR2XML

## Slide 15: c) simple functional scheme
2. General features
User’s
experiment choices
User’s information about model/lab
CMIP6 Data Request (DR)
MIPs
experiments
institutions
models, …
Thesaurus:
CMOR name
shape
frequency
compute method (ex. temporal mean, spatial mean, masking)
metadata (ex. long name, standard name, units, description)
For each variable, get:
« List » of variables to output
uses
configures
queries
builds
implements
XIOS spatial and temporal filters
MP XIOS-dr2xml Training, 15-19 March 2021 14
XIOS
file_def.xml
glues
CMOR standard attributes
Data Reference Syntax (DRS)
CMIP6 Controlled Vocabulary (CV)
File naming + tree directory conventions
One per context (one context per model component)
Requested output variables according to the experiment [priority level, member, period], chosen
DR2XML

## Slide 16: c) simple functional scheme (cont.)
2. General features
MP XIOS-dr2xml Training, 15-19 March 2021 15
XIOS
file_def.xml
XIOS
file_def.xml
XIOS
file_def.xml
XIOS
file_def.xml
atmos
land
sea-ice
ocean

## Slide 17: c) simple functional scheme (cont.)
2. General features
MP XIOS-dr2xml Training, 15-19 March 2021 16
XIOS
file_def.xml
XIOS
file_def.xml
XIOS
file_def.xml
XIOS
file_def.xml
atmos
land
sea-ice
iodef.xml
ocean
included in

## Slide 18: c) simple functional scheme (cont.)
2. General features
MP XIOS-dr2xml Training, 15-19 March 2021 17
XIOS
file_def.xml
XIOS
file_def.xml
XIOS
file_def.xml
XIOS
file_def.xml
atmos
land
Coupled Model
sea-ice
iodef.xml
XIOS
cpl
XIOS
XIOS
XIOS
atmos
land
sea-ice
ocean
ocean
included in

## Slide 19: c) simple functional scheme (cont.)
2. General features
MP XIOS-dr2xml Training, 15-19 March 2021 18
Ready to be published on ESGF.
XIOS
file_def.xml
XIOS
file_def.xml
XIOS
file_def.xml
XIOS
file_def.xml
atmos
land
Coupled Model
sea-ice
iodef.xml
XIOS
cpl
XIOS
XIOS
XIOS
atmos
land
sea-ice
ocean
ocean
included in
writes
writes
one file per physical field
append write
(-> split_freq)
Simultaneous writing of netCDF files (2nd level XIOS servers)
NetCDF files
NetCDF files
NetCDF files
NetCDF files
atmos
land
ocean
sea-ice

## Slide 20: d) the ping files
2. General features
MP XIOS-dr2xml Training, 15-19 March 2021 19
Coupled Model
XIOS
cpl
XIOS
XIOS
XIOS
atmos
land
sea-ice
ocean
CMIP6 Data Request (DR)
Standard variable names

## Slide 21: d) the ping files
2. General features
MP XIOS-dr2xml Training, 15-19 March 2021 20
Coupled Model
XIOS
cpl
XIOS
XIOS
XIOS
atmos
land
sea-ice
ocean
CMIP6 Data Request (DR)
Standard variable names
XIOS field_def.xml
Model output variable native names
(xios_send_field)
XIOS field_def.xml
XIOS field_def.xml
XIOS field_def.xml
atmos
land
sea-ice
Written once for all

## Slide 22: d) the ping files
2. General features
MP XIOS-dr2xml Training, 15-19 March 2021 21
Coupled Model
XIOS
cpl
XIOS
XIOS
XIOS
atmos
land
sea-ice
ocean
CMIP6 Data Request (DR)
Standard variable names
XIOS field_def.xml
Model output variable native names
(xios_send_field)
XIOS field_def.xml
XIOS field_def.xml
XIOS field_def.xml
ping_file.xml
ping_file.xml
ping_file.xml
atmos
atmos
land
land
ocean
sea-ice
ocean
sea-ice
ping_file.xml
correspondence
correspondence
Written once for all
Written once for all

## Slide 23
1.3 CMOR Variable: [sos] Sea Surface Salinity
label : sos
vid : [var] sos [74a9891bcab2667dbcb66574c6370c86]
title : Sea Surface Salinity
defaultPriority : 1
modeling_realm : ocean
type : real
2.3 Dimensions and related information [stid ]: Temporal mean, Global field (single level) [XY-na] [amse-tmn] [str-a098]
processing : Report on native horizontal grid as well as on a spherical latitude/longitude grid.
frequency : mon
rowIndex : 22
mipTable : Omon
description : Sea water salinity is the salt content of sea water, often on the Practical Salinity Scale of 1978. However, the unqualified term 'salinity' is generic and does not necessarily imply any particular method of calculation. The units of salinity are dimensionless and the units attribute should normally be given as 1e-3 or 0.001 i.e. parts per thousand.
[…]
2.3 Dimensions and related information: [str-a098] Temporal mean, Global field (single level) [XY-na] [amse-tmn]
label : str-a098
spid : [spatialShape] XY-na [a656047a-8883-11e5-b571-ac72891c3257]
title : Temporal mean, Global field (single level) [XY-na] [amse-tmn]
cell_methods : area: mean where sea time: mean
cell_measures : area: areacello
description : For time mean fields, it may be useful to add information about the sampling interval in the cell_methods string. The syntax is to append, in brackets, 'interval: *amount* *units*', for example 'area: time: mean (interval: 1 hr)'. The units must be valid UDUNITS, e.g. day or hr.
[…]
e) “sos_Omon” example (DR info.)
2. General features
1.2 MIP Variable: [sos] Sea Surface Salinity
label : sos
provmip : [mip] OMIP [OMIP]
prov : OMIP.day
units : 0.001
title : Sea Surface Salinity
uid : 74a9891bcab2667dbcb66574c6370c86
procnote : ('',)
procComment :
1.8 CF Standard Names [sn ]: SeaSurfaceSalinity
description : […]
1.8 CF Standard Names: [SeaSurfaceSalinity] Sea Surface Salinity
units : 1e-3
label : SeaSurfaceSalinity
title : Sea Surface Salinity
uid : sea_surface_salinity
description : […]
MP XIOS-dr2xml Training, 15-19 March 2021 22

## Slide 24: e) “sos_Omon” example
2. General features
MP XIOS-dr2xml Training, 15-19 March 2021 23
CMIP6 Data Request (DR)
XIOS field_def.xml
ping_file.xml
ocean
ocean
XIOS
file_def.xml
ocean
DR2XML
<field id= "CMIP6_sos” field_ref= "sss” > this * $convSpsu </field>
<field id= "sss" long_name= "sea surface salinity" standard_name= "sea_surface_salinity" unit= "1e-3" />
<file id= "sos_Omon_gn" name= "sos_Omon_CNRM-CM6-1_historical_r1i1p1f1_gn_%start_date%-%end_date%" output_freq= "1mo" append="true" […] >
Requests monthly mean of ocean sea surface salinity (sos_Omon) for DECK/historical simulation
<field id= "CMIP6_sos_average” field_ref ="CMIP6_sos" operation= "average” />
<field name= "sos" field_ref= "CMIP6_sos_average" operation="average" detect_missing_value="True" default_value="1.e+20" prec="4" cell_methods="area: mean where sea time: mean" cell_methods_mode="overwrite"> […] </field>
</file>
[…]
[…]
Let’s say we want to prepare file-def for the DECK/historical CMIP6 experiment, for the nemo context…
<!-- Conversion factor for salinity into PSU ( 35. / 35.16504 ) -->
<variable id="convSpsu" type="float" > 0.9953067 </variable>

## Slide 25: e) “sos_Omon” example (cont.)
2. General features
MP XIOS-dr2xml Training, 15-19 March 2021 24
XIOS
file_def.xml
ocean
Arpege/Surfex: 28 758 lines !
Nemo/Gelato: 14 840 lines !
Trip: 383 lines
CNRM-CM6 coupled model

## Slide 26: a) installation
3. Usage
GR XIOS-dr2xml Training, 15-19 March 2021 25
Dr2xml (+ XlsXwritter, six)
dreqPy (the CMIP6 Data Request)
CMIP6_CVs
$ git clone https://github.com/rigoudyg/dr2xml.git
$ pip install –upgrade [--user] dreqPy==01.00.32
$ git clone https://github.com/WCRP-CMIP/CMIP6_CVs
$ svn co http://proj.badc.rl.ac.uk/svn/exarch/CMIP6dreq/tags/01.00.32
or :

## Slide 27: b) configuration
3. Usage
GR XIOS-dr2xml Training, 15-19 March 2021 26
2 files of dr2xml settings (python dictionaries)
a set of model related XML files for XIOS : context, domains, field_defs
additional XML files, the so-called “ping_files” (one per context)

## Slide 28: c) execution
3. Usage
GR XIOS-dr2xml Training, 15-19 March 2021 27

## Slide 29: d) verification
3. Usage
GR XIOS-dr2xml Training, 15-19 March 2021 28
Skipped variables (i.e. whose alias is not present in the pingfile):
>>> TABLE: Ofx 03/09 ----> sftof(1) ugrid(1) volcello(1)
>>> TABLE: SImon 01/20 ----> sirdgconc(1)
>>> TABLE: Omon 03/37 ----> msftmz(1) msftmzmpa(1) vsf(1)
Some Statistics on actually written variables per frequency+shape...
EmonZ P1 1 : ['sltbasin']
Omon P1 1 : ['hfbasin']
Omon P2 2 : ['htovgyre', 'htovovrt']
mon YB-na -------- --- 4
Omon P1 10 : ['bigthetao', 'so', 'thetao', 'thkcello’, 'umo’, 'uo', 'vmo', 'vo', 'wmo', 'wo']
mon XY-O -------- --- 10
PrimOday P1 1 : [u'so']
day XY-O -------- --- 1
Some Statistics on actually written variables per variable...
-----------------------
--- VARNAME: bigthetao : Sea Water Convervative Temperature
-----------------------
* mon_Omon_XY-O_1
----------------
--- VARNAME: so : Sea Water Salinity
----------------
* mon_Omon_XY-O_1
* day_PrimOday_XY-O_1.0
2 user-friendly views in dr2xml log file
…That does not exempt from looking carefully at the generated file-def !
$ cd DR2XML/dr2xml_training
$ jupyter-notebook
dr2xml_training
exercice1

## Slide 30: a) basic functions
4. Functionalities
Spatial:
  remapping on different grids
  regridding on pressure levels
  regridding on height levels (in next version, sept. 2021)
  interpolation at observation sites
  meridional/zonal means
Temporal:
  sampling period
  time mean / time point
  diurnal cycle
GR XIOS-dr2xml Training, 15-19 March 2021 29
“basic functions” : ordinated and optimised combination of XIOS filters automatically implemented according to the specifications of the data request.
Chaining and combination of both
XIOS ready to compute/output requested diagnostics according to the DR compute specification

## Slide 31: b) customisation
4. Functionalities
Filtering options :
  curation : can filter out variables that are requested twice
  selection :
    filtering on experiment, on simulated year, or both
    choosing the maximum priority level of variables to output
  exclusion/inclusion : user can also provide lists of excluded/included…
    variables (var)
    tables (tbl)
    pairs (var,tbl)
    spatial shapes
  metadata filtering : user can take the control on attributes to write in the NetCDF files
GR XIOS-dr2xml Training, 15-19 March 2021 30
$ cd DR2XML/dr2xml_training
$ jupyter-notebook
exercice2

## Slide 32: b) customisation (cont.)
4. Functionalities
Add methods :
  dr2xml allows to output additional variables = the so-called “home data request”
    “cmor” variables : defined in the Data Request but not requested for this experiment
    “extra” variables : defined through additional tables and which are not “cmor”
    “dev” variable : for development purpose, can be used to output variables with a minimal set of arguments
  The “home data request” was used during CMIP6 production as a “safety net” to compensate DR potential lacks
MP XIOS-dr2xml Training, 15-19 March 2021 31
$ cd DR2XML/dr2xml_training
$ jupyter-notebook
exercice3

## Slide 33: c) extended usage
4. Functionalities
Dr2xml for daily research production
  discipline : Adopt the good practices using the CMOR/CMIP6 standards, even for non CMIP6 production
  flexibility : The user can free more or less from the DR, choosing to :
    make a new simulation with the same output variables as in a given CMIP6 experiment
    ignore all of from the CMIP6 DR and only specify its own outputs via the “home data request”
Adaptation to other projects like CORDEX
  new functionalities implemented (e.g. interpolation to altitude level)
  other needs to be instructed… (in IS-ENES3 framework)
MP XIOS-dr2xml Training, 15-19 March 2021 32
$ cd DR2XML/dr2xml_training
$ jupyter-notebook
exercice4

## Slide 34: summary
Dr2xml
XIOS-dr2xml Training, 15-19 March 2021 33
DR-dr2xml-XIOS pipeline is designed to facilitate the configuration of XIOS-enabled climate models contributing to CMIP exercises
Is the best way to conform (as far as we can) to a data request as complex as the CMIP6 one
Scraps the nightmare of a “by hand” model output configuration
Dynamic analyse of the simulated period and adaptation of output configuration consequently
Files written by XIOS configured by dr2xml are CMIP6-compliant
Avoid the CMORisation step in the data production workflow
Can be used as well for daily research simulations, benefitting (or not…) from the CMIP6 standards
Without CMIP6 and the Data Request dr2xml won’t have existed, even less without XIOS, but now we’ve got it, sounds there is a life (for it) after CMIP6 !

## Slide 35: The End.
XIOS-dr2xml Training, 15-19 March 2021 34
Thanks to all for your participation !
Any questions ?
Keep in touch !
gaelle.rigoudy@meteo.fr
moine@cerfacs.fr
DR2XML
xiostraining2021.slack.com